Invitation for Prequalification

Date: February 26, 2016

Loan Agreement No: AZB-P4

IFP No: JICA.AZB P-4. W/C-5

- The Government of the Republic of Azerbaijan has received Loan from Japan International Cooperation Agency towards the cost of the Provincial Cities Water Supply and Sewerage Project It is intended that part of the proceeds of this Loan will be applied to eligible payments under the contract resulting from the bidding for which this prequalification is conducted.

- The Azersu Open Joint Stock Company intends to prequalify contractors and/or firms for Package W5: Design and Construction of Waste Water Treatment Plant (WWTP) for Naftalan.

The scope of work shall be summarized as follows:

- Design and Construction of Waste Water Treatment Plant;

-	Pre-treatment facilities flow: 21,000 m3/day

-	Total bio-treatment facility flow: 6,000 m3/day

-	Construction phase: 2 phases

-	Bio-treatment facilities flow for first phase: 3,000 m3/day

Since Naftalan WWTP is planned to be constructed in two phases, design flow of the first phase for bio-treatment facilities shall be covered by the Contract.

- Administration building in WWTP premises;

- Provision of spare parts and equipment;

- Leveling, grading and asphalt pavement of existing access road for WWTP site;

L 1300m x W6m

- Design and construction of external power supply from sub-station to WWTP site;

- Operation and Maintenance;

Operation and maintenance of wastewater treatment plants for one year from the date of operational acceptance after successful completion of the Guarantee Test

- Training;

Provision of training to the Employer

- It is expected that Invitation for Bids will be made in April 2016.

- Prequalification will be conducted through prequalification procedures specified in the Guidelines for Procurement under Japanese ODA Loans, October 1999, and is open to all bidders from eligible source countries, as defined in the guidelines.

- Interested eligible Applicants may obtain further information from and inspect the Prequalification Documents at the address given below from 10:00 and 17:00 (AZT, GMT +4h), except for Saturday and Sunday.

- A complete set of prequalification documents may be obtained by interested Applicant(s) on the submission of a written application to the address below and upon payment of a non-refundable fee of 320 AZN or 200 USD by direct deposit to the following account No:

Beneficiary’s Name:		AZERSU OJSC

INTP:				9900001751

Beneficiary’s Bank:		Kapital Bank of Azerbaijan Republic, Nasimi branch No 1

INTP:				9900003611

Local currency account No:	AZ65AIIB33070019441100216111

Foreign currency account 	AZ55AIIB33170018401100216111

Code:				200112

SWIFT Code:			AIIBAZ2X

- Applications for prequalification should be submitted in sealed envelopes, delivered to the address below by April 19, 2016 and be clearly marked “Application to Prequalify for Provincial Cities Water Supply and Sewerage Project, Package W5: Design and Construction of Waste Water Treatment Plant (WWTP) for Naftalan”.

Azersu Open Joint Stock Company

Attention: Mr. Tagiyev Ilgar, Head of Tenders and International

Project Management Department

Address: 67 Moscow Avenue, Baku AZ1012, Azerbaijan

Telephone: +994 12 431 4767 (1033)

Fax: +994 431 47 92

E-mail: i.tagiyev@azersu.az